Scope and Applicability

This procedure applies to projects/activities involving the use of cranes. The purpose of this procedure is to establish safe practices for the operation and maintenance of cranes in order to minimize the potential for personal injury and property damage.

Implementation

Shop Activities:	Implementation of this procedure is the responsibility of the Shop Manager/Foreman.

Field Activities: 	Implementation of this procedure is the responsibility of the Project Manager/Superintendent.

Procedure

1.0	General

A.	Allow only qualified, licensed operators to operate cranes.

B.	Obtain annual inspection certification prior to use of any crane.

C.	Designate a Competent Person to perform a Pre-Acceptance Inspection prior to accepting a crane from a vendor or owner. See Appendices B, C, and D.

D.	Keep manufacturer’s Operator’s Manual in the cab of the crane.

E.	Comply with manufacturer’s specifications and limitations for the operation of all cranes.

F.	Never modify a crane without the manufacturer’s written approval.

G.	Repair booms in accordance with manufacturer’s specifications only.

H.	Provide an easily accessible fire extinguisher with a minimum rating of 5 B:C in the cab of each crane.

I.	Provide safety latches for all load hooks.

J.	Require that rated load capacities, recommended operating speeds, and special hazard warnings are posted on the crane in a place visible to the operator while at the controls.

K.	Down-rate load ratings by 2% for each degree of temperature below zero degrees Fahrenheit (-18 degrees C) until minus 30 degrees (-34 degrees C) is attained.

L.	Do not make lifts when the temperature is minus 30 degrees (-34 degrees C) or below.

M.	Determine the weight of the lift to within 5% prior to making the lift. When determining the weight, consider all handling devices, i.e. rigging, load block, and load line from the tip of the boom to the load, as part of the load.

N.	Test the crane’s brakes by raising the load a few inches (5 cm) and applying the brakes each time a load approaches the crane’s rated capacity.

O.	Consider wind loads when making lifts (see Appendix A).

P.	Always barricade the swing radius of the superstructure.

Q.	Perform and record results of air monitoring for toxic gases and oxygen deficiency when using equipment in, or equipment exhausts into, enclosed spaces.

R.	Restrict side loading to freely suspended loads.

S.	Use taglines at all times unless impractical.

T.	Require that all jibs are equipped with positive stops to prevent their movement of more than 5% above the straight line of the jib and boom.

U.	Designate a competent person to provide hand signals to the operator, and post a hand signals chart at the jobsite.

1.	The crane operator must take signals only from the designated signalman.

V.	Never allow personnel under the load or swing a load over personnel.

W.	Sound the horn when swinging loads.

X.	Prohibit all personnel from riding the hook, ball, load block, or load.

Y.	Require that the house swing is locked when leaving the crane unattended, even if for only short periods of time.

Z.	Tie the main hook off to a secure anchor at the end of each shift.

AA.	Boom cranes should be down and resting on a suitable support when high winds are likely overnight.

BB.	Ground personnel observe clearances when the operator’s visibility is obscured or when traveling the crane.

CC.	Deenergize electrical power lines, as feasible, or provide insulating barriers when working proximate to power lines.

DD.	When working in proximity to energized power lines which have not been provided with insulating barriers, refer to SMS “Utility Clearances”.

EE.	Require that transmission towers are de-energized, or crane and load are properly grounded when working near transmitters where an electrical charge can be induced.

2.0	Truck Cranes

A.	Never lift a load beyond the tipping point, which is the moment the wheels opposite the load leave their initial, unloaded position.

B.	Require that the crane is level to within 1/8 inch (3 mm) in 24 inches (61 cm).

C.	Fully extend all outriggers and lift carrier wheels until they just clear the ground.

D.	Use timbers that are larger than the dimensions of the outrigger pads under the outrigger pads when ground conditions are less than ideal.

E.	Never use the front bumper counterweight to increase lifting capacity unless it is indicated in the load capacity chart.

F.	Do not lift a load over the front of a truck crane unless the crane’s manufacturer approves such a lift.

G.	Use nylon slings when handling tubular chord boom sections to avoid damage to the chords and lattice.

H.	Assemble and disassemble pin-connected booms in accordance with SMS  “Rigging.”

3.0	Crawler Cranes

A.	Never lift a load beyond the tipping point, which is the moment the track rollers leave the roller path opposite the load.

B.	Require that the crane is level to within 1/8 inch in 24 inches.

C.	Make turns on hard, level ground only.

D.	Use special care and a suitable safety holdback device when traveling up or down steep slopes.

E.	Require that drive chains are always to the rear of the crane when traveling or lifting.

F.	Use blocks against the sprocket or idler when lifting a load over the front or rear of the crane.

G.	Use timber mats when ground conditions are less than ideal. Position mats crosswise to the tracks.

H.	Install traction bars when the work area is covered with ice or snow.

I.	Reduce rated loads by 20% when traveling with load over side of crawler or when traveling and swinging simultaneously.

J.	Use nylon slings when handling tubular chord boom sections to avoid damage to the chords or lattice.

K.	Assemble and disassemble pin-connected booms in accordance with SMS “Rigging”.

4.0	Hydraulic Cranes

A.	Never lift a load over the side unless all outriggers have been set.

B.	Never lift a load over the front unless all outriggers have been set.

C.	Engage the mechanical swing lock and reduce travel speed to creep speed when traveling with loads that approach the crane’s capacity (on rubber rating).

D.	Tie all loads being carried to the front of the crane.

E.	Extend all power telescoping boom sections equally.

F.	Always use an anti two-blocking device.

G.	Provide back-up alarms.

H.	Inflate tires to recommended pressure before lifting on rubber.

I.	Do not permit “on rubber” lifting with the boom extended.

5.0	Critical Lift Permits

A.	Require a completed Critical Lift Permit (Appendix I) prior to all lifts that meet any of the following conditions:

    - Lifts over live process lines, critical equipment, high voltage power lines, or other lifts that may jeopardize personnel and/or plant operations.

    - Lifts of 25,000 pounds or greater.

    - Multi-crane lifts.

    - Single crane lifts exceeding 75% of the crane’s rated capacity, regardless of weight.

    - Man basket lifts (Refer to SMS “Crane Suspended Personnel Platforms”).

6.0	Inspections

A.	Designate a Competent Person to inspect all cranes in accordance with the following Appendices:

1.	Crawler Crane Pre-Acceptance Inspection (Appendix B).

2.	Truck Crane Pre-acceptance Inspection (Appendix C).

3.	Hydraulic Crane Pre-Acceptance Inspection (Appendix D).

4.	Daily Equipment Checklist - All Cranes (Appendix E).

5.	Monthly Crawler Crane Inspection (Appendix F).

6.	Monthly Hydraulic Crane Inspection (Appendix G).

7.	Wire Rope Inspection (Appendix H).

8.	Annual Inspection/Certification (3rd Party)

7.0	Documentation Summary

A.	File these documents in the Project/Shop Safety and Health File:

    - Operator’s qualifications and licenses.

    - Copies of all inspections required by Subsection E, “Inspections”.

    - Air monitoring results, as applicable.

    - Critical Lift Permits.

B.	The Risk Management Center is to be used to document all information including the following:

| Documents | Risk Management Center Location |
| --- | --- |
| Written Crane Operation Program | My ContentTM |
| Training Documentation including: - Classroom training and training course completed - Sign-in sheets - Quizzes - Skills evaluations - Operator Certificates | Training TrackTM application |
| Pre-shift Inspection Checklists | My ContentTM |
| Safety Observations | Job Hazard Analysis/ Safety Observation ToolTM |
| Near misses | Incident TrackTM |
| Accidents and claims | Incident TrackTM |
| Supplier and manufacturer Certificates of Insurance | COI TrackTM |
| Safety Data Sheets | SDS TrackTM |

### Appendix A: Wind Loads

The wind pressure (P) in pounds per square foot on a flat surface normal to the direction of the wind for any given velocity (V) in miles per hour is given quite accurately by the formula

P = 0.004 V

The following table gives the pressure per square foot on a flat surface normal to the direction of the wind for different velocities, as calculated by the formula.

#### Velocity, miles		                	                 Pressure, lbs.

per hour		            	                    		per sq. ft.

10							  	0.4

20                                  				1.6

30							   	3.6

Use the formula above to calculate the pressure per square foot times the load area. Lifting is not permitted with wind velocity above 30mph, or if the force exceeds 2% of the crane’s chart capacity.

Appendix B: Pre-Acceptance Or Release Crawler Crane Inspection Report

| Make | Model | Basic Capacity | Serial Number |
| --- | --- | --- | --- |
| Vendor | Inspection Location | Date | Order Number |
| Remarks: |  |  |  |

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
| GENERAL |
|  | Appearance |  |  |  |  |
|  | Paint |  |  |  |  |
|  | Glass |  |  |  |  |
|  | Grease & oil leaks |  |  |  |  |
|  | Rating chart |  |  |  |  |
|  | Load indicator |  |  |  |  |
|  | Fire Extinguisher |  |  |  |  |
| ENGINE (UPPER) |
|  | Oil level & condition |  |  |  |  |
|  | Starting equipment |  |  |  |  |
|  | Cooling system |  |  |  |  |
|  | Anti-freeze |  |  |  |  |
|  | Anti-icing equipment |  |  |  |  |
|  | Battery condition |  |  |  |  |
|  | Air system |  |  |  |  |
|  | Hydraulic system |  |  |  |  |
|  | Engine instruments |  |  |  |  |

Appendix B: Pre-Acceptance Or Release Crawler Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
| TORQUE CONVERTER |
|  | Instruments |  |  |  |  |
|  | Temperature |  |  |  |  |
|  | Pressure |  |  |  |  |
| DRAW WORKS |
|  | Boom hoist |  |  |  |  |
|  | Clutch |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Swing/friction |  |  |  |  |
|  | Swing/other |  |  |  |  |
|  | House lock |  |  |  |  |
|  | Travel |  |  |  |  |
|  | Turning dogs |  |  |  |  |
|  | Main hoist |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Power down |  |  |  |  |
|  | Auxiliary hoist |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Third drum |  |  |  |  |
|  | Brake |  |  |  |  |
| LOWER WORKS |
|  | House rollers |  |  |  |  |
|  | Hook rollers |  |  |  |  |
|  | Roller path |  |  |  |  |
|  | Track pads |  |  |  |  |
|  | Track pins |  |  |  |  |
|  | Tumblers |  |  |  |  |
|  | Rollers |  |  |  |  |

Appendix B: Pre-Acceptance Or Release Crawler Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Idlers |  |  |  |  |
|  | Sprockets |  |  |  |  |
|  | Chains |  |  |  |  |
|  | Track adjustment |  |  |  |  |
| BOOM No. __________ Length ____________ |
|  | Point sheaves |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Load line dead end |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Boom connections |  |  |  |  |
|  | Boom stops |  |  |  |  |
|  | Boom cutout |  |  |  |  |
|  | Boom angle indicator |  |  |  |  |
| JIB No. ______________ Length ______________ |
|  | Point sheave |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Connections |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Stops |  |  |  |  |
|  | Strut |  |  |  |  |
| MAST No. __________ Length _____________ |
|  | Point sheaves |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Connections |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |

Appendix B: Pre-Acceptance Or Release Crawler Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Stops |  |  |  |  |
|  | Pendants/guy Lines |  |  |  |  |
| GANTRY |
|  | Sheaves |  |  |  |  |
|  | Pins |  |  |  |  |
| EQUALIZER |
|  | Sheaves |  |  |  |  |
|  | Pins |  |  |  |  |
| MAIN LOAD BLOCK Capacity: __________ |
|  | Sheaves |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Hook/shackle |  |  |  |  |
|  | Safety latch |  |  |  |  |
| AUXILIARY LOAD |
|  | Headache ball |  |  |  |  |
|  | Drop block |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Safety latch |  |  |  |  |
| COUNTERWEIGHTS Specify Weight |
|  | Crane counterweight |  |
|  | Auxiliary counterweight |  |
|  | Car body counterweight |  |
|  | Locking devices |  |
| WIRE ROPE Specify Type |
|  | Main load line |  |
|  | Auxiliary load line |  |
|  | Boom hoist line |  |
|  | Boom pendants |  |

Appendix B: Pre-Acceptance Or Release Crawler Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Jib pendants |  |
| Does crane meet current inspection and certification requirements: |
| Has boom and jib been N.D.T. tested? Certify |
| Have load hooks/shackles been N.D.T. tested? Certify |
| Has boom or jib been repaired? Specify |

SUMMARY OF INSPECTION

I acknowledge this inspection report to show the condition of the above equipment. This report shall be used as reference to determine the repairs to be made during the rental period and at the termination of the rental period.

Inspector:

Approval:

Vendor's approval to inspection report:

Appendix C: Pre-Acceptance or Release Truck Crane Inspection Report

| Make | Model | Basic Capacity | Serial Number |
| --- | --- | --- | --- |
| Vendor | Inspection Location | Date | Order Number |
| Remarks: |  |  |  |

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
| GENERAL |
|  | Appearance |  |  |  |  |
|  | Paint |  |  |  |  |
|  | Glass |  |  |  |  |
|  | Grease & oil leaks |  |  |  |  |
|  | Rating chart |  |  |  |  |
|  | Load indicator |  |  |  |  |
|  | Fire Extinguisher |  |  |  |  |
| ENGINE (UPPER) |
|  | Oil level & condition |  |  |  |  |
|  | Starting equipment |  |  |  |  |
|  | Cooling system |  |  |  |  |
|  | Anti-freeze |  |  |  |  |
|  | Anti-icing equipment |  |  |  |  |
|  | Battery condition |  |  |  |  |
|  | Air system |  |  |  |  |
|  | Hydraulic system |  |  |  |  |

Appendix C: Pre-Acceptance or Release Truck Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Engine instruments |  |  |  |  |
| TORQUE CONVERTER |
|  | Instruments |  |  |  |  |
|  | Temperature |  |  |  |  |
|  | Pressure |  |  |  |  |
| DRAW WORKS |
|  | Boom hoist |  |  |  |  |
|  | Clutch |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Swing/friction |  |  |  |  |
|  | Swing/other |  |  |  |  |
|  | House lock |  |  |  |  |
|  | Main hoist |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Power down |  |  |  |  |
|  | Auxiliary |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Third drum |  |  |  |  |
|  | Brake |  |  |  |  |
| CARRIER |
|  | Outrigger beams |  |  |  |  |
|  | Outrigger cylinders |  |  |  |  |
|  | Outrigger floats |  |  |  |  |
|  | Tires |  |  |  |  |
|  | Lights |  |  |  |  |
|  | Brakes |  |  |  |  |
|  | Steering |  |  |  |  |
|  | Sprockets |  |  |  |  |

Appendix C: Pre-Acceptance or Release Truck Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Chains |  |  |  |  |
|  | Track adjustment |  |  |  |  |
| ENGINE (LOWER) |
|  | Starting equipment |  |  |  |  |
|  | Cooling system |  |  |  |  |
|  | Air system |  |  |  |  |
|  | Instruments |  |  |  |  |
| BOOM No. __________ Length ____________ |
|  | Point sheaves |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Load line dead end |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Boom connections |  |  |  |  |
|  | Boom stops |  |  |  |  |
|  | Boom cutout |  |  |  |  |
|  | Boom angle indicator |  |  |  |  |
| JIB No. ______________ Length ______________ |
|  | Point Sheave |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Connections |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Stops |  |  |  |  |
|  | Strut |  |  |  |  |
| MAST No. __________ Length _____________ |
|  | Point sheaves |  |  |  |  |
|  | Sheave guards |  |  |  |  |

Appendix C: Pre-Acceptance or Release Truck Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Connections |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Stops |  |  |  |  |
|  | Pendants/guy lines |  |  |  |  |
| GANTRY |
|  | Sheaves |  |  |  |  |
|  | Pins |  |  |  |  |
| EQUALIZER |
|  | Sheaves |  |  |  |  |
|  | Pins |  |  |  |  |
| MAIN LOAD BLOCK Capacity: __________ |
|  | Sheaves |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Hook/shackle |  |  |  |  |
|  | Safety latch |  |  |  |  |
| AUXILIARY LOAD |
|  | Headache ball |  |  |  |  |
|  | Drop block |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Safety latch |  |  |  |  |
| COUNTERWEIGHTS Specify Weight |
|  | Crane counterweight |  |
|  | Auxiliary counterweight |  |
|  | Car body counterweight |  |
|  | Locking devices |  |
| WIRE ROPE Specify Type |
|  | Main load line |  |

|  | Auxiliary load line |  |
| --- | --- | --- |
|  | Boom hoist line |  |
|  | Boom pendants |  |
|  | Jib pendants |  |
| Does crane meet current inspection and certification requirements: |
| Has boom and jib been N.D.T. tested? Certify |
| Have load hooks/shackles been N.D.T. tested? Certify |
| Has boom or jib been repaired? Specify |

SUMMARY OF INSPECTION

I acknowledge this inspection report to show the condition of the above equipment. This report shall be used as reference to determine the repairs to be made during the rental period and at the termination of the rental period.

Inspector:

Approval:

Vendor's approval to inspection report:

Appendix D: Pre-Acceptance or Release Hydraulic Crane Inspection Report

| Make | Model | Basic Capacity | Serial Number |
| --- | --- | --- | --- |
| Vendor | Inspection Location | Date | Order Number |
| Remarks: |  |  |  |

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
| GENERAL |
|  | Appearance |  |  |  |  |
|  | Paint |  |  |  |  |
|  | Glass |  |  |  |  |
|  | Glass wipers |  |  |  |  |
|  | Grease & oil leaks |  |  |  |  |
|  | Rating chart |  |  |  |  |
|  | Load indicator |  |  |  |  |
|  | Fire Extinguisher |  |  |  |  |
| ENGINE |
|  | Oil level & condition |  |  |  |  |
|  | Starting equipment |  |  |  |  |
|  | Cooling system |  |  |  |  |
|  | Anti-freeze |  |  |  |  |
|  | Anti-icing equipment |  |  |  |  |
|  | Battery condition |  |  |  |  |
|  | Air system |  |  |  |  |
|  | Hydraulic system |  |  |  |  |

Appendix D: Pre-Acceptance or Release Hydraulic Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Engine instruments |  |  |  |  |
|  | Electrical system |  |  |  |  |
| CARRIER |
|  | Steering assemblies |  |  |  |  |
|  | Brakes |  |  |  |  |
|  | Outriggers |  |  |  |  |
|  | Outrigger pads |  |  |  |  |
|  | Tires |  |  |  |  |
|  | Lights |  |  |  |  |
| UPPER |
|  | Main swing assembly |  |  |  |  |
|  | Swing lock |  |  |  |  |
|  | Main hoist |  |  |  |  |
|  | Main hoist brake |  |  |  |  |
|  | Auxiliary hoist |  |  |  |  |
|  | Auxiliary hoist brake |  |  |  |  |
|  | Boom hoist |  |  |  |  |
| BOOM No. __________ Length ____________ |
|  | Boom sections |  |  |  |  |
|  | Point sheaves |  |  |  |  |
|  | Anti two block device |  |  |  |  |
|  | Boom angle indicator |  |  |  |  |
| JIB No. ______________ Length ______________ |
|  | Point sheave |  |  |  |  |
|  | Stow lock |  |  |  |  |
|  | Connections |  |  |  |  |
| MAIN LOAD BLOCK |
|  | Sheaves |  |  |  |  |

Appendix D: Pre-Acceptance or Release Hydraulic Crane Inspection Report (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Swivel |  |  |  |  |
|  | Hook/shackle |  |  |  |  |
|  | Safety latch |  |  |  |  |
| AUXILIARY LOAD Capacity ___________ |
|  | Ball |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Hook/swivel |  |  |  |  |
|  | Safety latch |  |  |  |  |
| WIRE ROPE Specify type: ___________________ |
|  | Main load line |  |  |  |  |
|  | Auxiliary load line |  |  |  |  |
| Does crane meet current inspection and certification requirements: |
| Has boom and jib been N.D.T. tested? Certify |
| Have load hooks/shackles been N.D.T. tested? Certify |
| Has boom or jib been repaired? Specify |

SUMMARY OF INSPECTION

I acknowledge this inspection report to show the condition of the above equipment. This report shall be used as reference to determine the repairs to be made during the rental period and at the termination of the rental period.

Inspector:

Approval:

Vendor's approval to inspection report:

Appendix E: Equipment Check List (Daily)

| MAKE | MODEL | UNIT NUMBER | WEEK ENDING |
| --- | --- | --- | --- |

| CHECK ITEM | MONDAY | TUESDAY | WEDNESDAY | THURSDAY | FRIDAY | SATURDAY |
| --- | --- | --- | --- | --- | --- | --- |
| Engine oil |  |  |  |  |  |  |
| Lubrication |  |  |  |  |  |  |
| Starting system |  |  |  |  |  |  |
| Instruments |  |  |  |  |  |  |
| Cooling system |  |  |  |  |  |  |
| Air system |  |  |  |  |  |  |
| Hydraulic system |  |  |  |  |  |  |
| Operating controls |  |  |  |  |  |  |
| Glass, mirrors |  |  |  |  |  |  |
| Defroster, operating controls |  |  |  |  |  |  |
| Brakes |  |  |  |  |  |  |
| Steering system |  |  |  |  |  |  |
| Tires |  |  |  |  |  |  |
| Safety devices |  |  |  |  |  |  |
| Lights and reflectors |  |  |  |  |  |  |
| Horn |  |  |  |  |  |  |
| Windshield wipers |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |

These items are to be checked each morning before operating this piece of equipment. Report ALL items in need of repair to Maintenance Shop at the time of inspection. Turn in check sheet to Equipment Supervisor at beginning of the week.

Operator  			Badge Number

| DATE REPORTED | REPAIRS | DATE REPAIRED |
| --- | --- | --- |

Appendix F: Monthly Crawler Crane Inspection

| Make | Model | Unit Number | Date |
| --- | --- | --- | --- |

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
| GENERAL |
|  | Appearance |  |  |  |  |
|  | Paint |  |  |  |  |
|  | Glass |  |  |  |  |
|  | Grease & oil leaks |  |  |  |  |
|  | Rating chart |  |  |  |  |
|  | Load indicator |  |  |  |  |
|  | Fire Extinguisher |  |  |  |  |
| ENGINE(S) |
|  | Starting system |  |  |  |  |
|  | Air system |  |  |  |  |
|  | Instruments |  |  |  |  |
| TORQUE CONVERTER |
|  | Instruments |  |  |  |  |
| DRAW WORKS |
|  | Boom hoist |  |  |  |  |
|  | Clutch |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Swing/friction |  |  |  |  |
|  | Swing/other |  |  |  |  |
|  | House lock |  |  |  |  |
|  | Travel |  |  |  |  |
|  | Turning dogs |  |  |  |  |

Appendix F: Monthly Crawler Crane Inspection (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Main hoist |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Power down |  |  |  |  |
|  | Auxiliary hoist |  |  |  |  |
|  | Brake |  |  |  |  |
|  | Third drum |  |  |  |  |
|  | Brake |  |  |  |  |
| LOWER WORKS |
|  | House rollers |  |  |  |  |
|  | Hook rollers |  |  |  |  |
|  | Roller path |  |  |  |  |
|  | Track pads |  |  |  |  |
|  | Track pins |  |  |  |  |
|  | Tumblers |  |  |  |  |
|  | Rollers |  |  |  |  |
|  | Idlers |  |  |  |  |
|  | Sprockets |  |  |  |  |
|  | Chains |  |  |  |  |
|  | Track adjustment |  |  |  |  |
| BOOM |
|  | Point sheaves |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Load line dead end |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Boom connections |  |  |  |  |
|  | Boom stops |  |  |  |  |

Appendix F: Monthly Crawler Crane Inspection (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Boom cutout |  |  |  |  |
|  | Boom angle indicator |  |  |  |  |
| JIB |
|  | Point Sheave |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Connections |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Stops |  |  |  |  |
|  | Strut |  |  |  |  |
| MAST |
|  | Point sheaves |  |  |  |  |
|  | Sheave guards |  |  |  |  |
|  | Connections |  |  |  |  |
|  | Chords |  |  |  |  |
|  | Lattice |  |  |  |  |
|  | Stops |  |  |  |  |
|  | Pendants/guy lines |  |  |  |  |
| GANTRY |
|  | Sheaves |  |  |  |  |
|  | Pins |  |  |  |  |
| EQUALIZER |
|  | Sheaves |  |  |  |  |
|  | Pins |  |  |  |  |
| MAIN LOAD BLOCK |
|  | Sheaves |  |  |  |  |

Appendix F: Monthly Crawler Crane Inspection (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Swivel |  |  |  |  |
|  | Hook/shackle |  |  |  |  |
|  | Safety latch |  |  |  |  |
| AUXILIARY LOAD |
|  | Headache ball |  |  |  |  |
|  | Drop block |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Safety latch |  |  |  |  |
| WIRE ROPE Wire Rope Inspection Report Attached |

Inspected by:

Title:

Appendix G: Monthly Hydraulic Crane Inspection

| Make | Model | Unit Number | Date |
| --- | --- | --- | --- |

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
| GENERAL |
|  | Appearance |  |  |  |  |
|  | Paint |  |  |  |  |
|  | Glass |  |  |  |  |
|  | Grease & oil leaks |  |  |  |  |
|  | Fire extinguisher |  |  |  |  |
| ENGINE(S) |
|  | Starting equipment |  |  |  |  |
|  | Air system |  |  |  |  |
|  | Instruments |  |  |  |  |
| CARRIER |
|  | Steering system |  |  |  |  |
|  | Brakes |  |  |  |  |
|  | Outriggers |  |  |  |  |
|  | Tires |  |  |  |  |
|  | Lights |  |  |  |  |
|  | Backup alarm |  |  |  |  |
| UPPER |
|  | Swing assembly |  |  |  |  |
|  | Swing lock |  |  |  |  |
|  | Main hoist |  |  |  |  |
|  | Main hoist brake |  |  |  |  |
|  | Auxiliary hoist |  |  |  |  |
|  | Auxiliary hoist brake |  |  |  |  |

Appendix G: Monthly Hydraulic Crane Inspection (continued)

|  | CONDITION |  |
| --- | --- | --- |
|  | Good | Fair | Poor | NOTES |
|  | Boom cylinder(s) |  |  |  |  |
| BOOM |
|  | Boom sections |  |  |  |  |
|  | Point sheaves |  |  |  |  |
|  | Anti two block device |  |  |  |  |
|  | Boom angle indicator |  |  |  |  |
| JIB |
|  | Point Sheave |  |  |  |  |
|  | Stow lock |  |  |  |  |
| MAIN LOAD BLOCK |
|  | Sheaves |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Hook/shackle |  |  |  |  |
|  | Safety latch |  |  |  |  |
| AUXILIARY LOAD |
|  | Ball |  |  |  |  |
|  | Swivel |  |  |  |  |
|  | Hook/swivel |  |  |  |  |
|  | Safety latch |  |  |  |  |
| WIRE ROPE Use Wire Rope Inspection Report Attached |

Inspected by:

Title:

Appendix H: Wire Rope Inspection Report

| PROJECT | JOB NUMBER | MACHINE |
| --- | --- | --- |
| UNIT NUMBER | OWNER | OPERATOR |

| SERVICE | CONSTRUCTION | INSP. DATE | COL. 1 | CURRENT DIA. | COL. 2 | COL. 3 | COL. 4 | NOTES |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | ORIGINAL DIA. |  | LOSS OF DIA. | BROKEN WIRES IN ONE ROPE LAY | BREAKS IN 1 STRAND OF ONE LAY |  |
| Main hoist |  |  |  |  |  |  |  |  |
| Aux. hoist |  |  |  |  |  |  |  |  |
| Boom hoist |  |  |  |  |  |  |  |  |
| Boom pendants |  |  |  |  |  |  |  |  |
| Jib pendants |  |  |  |  |  |  |  |  |
| Main hoist |  |  |  |  |  |  |  |  |
| Aux. hoist |  |  |  |  |  |  |  |  |
| Boom hoist |  |  |  |  |  |  |  |  |
| Boom pendants |  |  |  |  |  |  |  |  |
| Jib pendants |  |  |  |  |  |  |  |  |
| Main hoist |  |  |  |  |  |  |  |  |
| Aux. hoist |  |  |  |  |  |  |  |  |
| Boom hoist |  |  |  |  |  |  |  |  |
| Boom pendants |  |  |  |  |  |  |  |  |
| Jib pendants |  |  |  |  |  |  |  |  |

NOTE: ANSI STANDARDS - ROPE MUST BE REMOVED FROM SERVICE WHEN DIAMETER LOSS OR WIRE BREAKAGE OCCURS AS FOLLOWS:

Appendix H: Wire Rope Inspection Report (continued)

| DIAMETER LOSS - COL. 1 & 2 |  | NUMBER OF WIRE BREAKS - COL 3 & 4 |
| --- | --- | --- |
| ALL EQUIPMENT EXCEPT FOR TOWER CRANES |  | EQUIPMENT | COL. 3 IN ONE ROPE LAY | COL. 4 IN ONE STRAND IN ONE ROPE LAY |
| ORIGINAL DIAMETER (INCH) | LOSS (INCH) |  | RUNNING ROPES CRANES AND DERRICKS | 6 | 3 |
| 3/4 (UP TO AND INCLUDING) 7/8 - 1 1/8 1 1/4 - 1 ½ | 3/64 1/16 3/32 |  | STANDING ROPES CRANES AND DERRICKS | 1 | 1 |
|  |  |  | ( ALSO REMOVE ROPE IF ONE OR MORE BREAKS IN THE VALLEY ARE EVIDENT |

Appendix I: Critical Lift Permit

# Project Name:		  Project Number:

Lift Location: ______________________ Time: ___________ Date:

Description of Load:

CRANE INFORMATION

## Manufacturer:		 Model Number: ___________________________

Boom/Jib Length:  Main Boom:                 ft.  Jib:		ft.	Total Boom: ___	_____ft.

Maximum Radius During Lift:  Pick:		 Swing:		Set:

## Direction and Degree of Swing:  From:  	To:	  Degrees:

Lift Elevation (0= Crane Support Elevation):  Maximum		ft.  Minimum:	ft.

Boom Angles (In Degrees): 	Pick:			Swing:			Set:

Jib Stowed?  Yes 	  No  		  Jib Erected?  Yes  			  No

Manufacturer’s Rated Capacity (per above configuration and radii): 	lbs.

### LOAD INFORMATION

## Weight of the Load:		lbs.    Effective Weight of Jib: 	lbs.

Effective Weight of Overhaul Ball (2X Ball Weight):  	 lbs.

Weight of Load Block:	lbs.       	Weight of Spreader	lbs.

Weight of Slings:  		lbs.  	Weight of Shackles:	lbs.

Weight of Other Rigging:  	lbs.	TOTAL LIFT WEIGHT:  	 lbs.

## LOAD PERCENT OF CRANE CAPACITY PER LOAD CHART:		%

_______________________________

Person Making Calculations	 Title	     	     		 Approved By		        Title