Objective: An evaluation of a forklift operator’s driving skills and habits

Set up a small course for trainees to go through. Require trainees to perform all functions of forklift operation (e.g., backing, raising and placing the load, moving with a load, moving through a blind spot, handling a pedestrian approaching the vehicle, etc.).

NOTE: Set up the course in a safe area away from others and traffic. Assure that all functions are supervised by a competent person who completes and certifies the evaluation.

Employee: ______________________________   Evaluator: ____________________________

Date: ___________________    Forklift training/quiz review date: _________________________

Employee written test passed: Yes _____   No _____

EVALUATION ITEM						_______		YES/NO_

- Completes pre-inspection to assure proper operation of equipment		________

- Drives at acceptable speeds				          			________

- Assures good visibility prior to moving through transition points, such as 
entrances or turns									________

- Looks behind before and while backing						________

- Operates equipment smoothly, without abrupt movement			________

- Properly secures loads								________

- Always keeps loads in a down position when moving				________

- Does not allow riders								________

- Put forks down and sets brake when forklift is stopped				________

- Uses a seat belt									________

- Slows at all transition points and uses the horn					________

- Stops at blind spots and beeps before proceeding					________

- Knows and never exceeds posted weight limits of forklifts, racks, shelves, 
or other storage areas								________

- Assures that the wheels of all trucks being loaded/unloaded are chocked	________

- Assures that back-up alarms are operative						________

- Drives with load facing uphill 							________

- Knows that lockout and the elimination of stored energy is required for 	
maintenance, service, or de-jamming work					________

- When fueling:

a. Controls ignition sources (e.g., no smoking, engine turned off, etc.) 		________

b. Properly places propane tanks with pin aligned 				________

c. Keeps lines and connections tight and leak-free 				________

d. Wears skin and eye protection for battery-handling				________

- Keeps everyone out of fall zone and away from suspended loads		________

- Approaches loads correctly to keep weight close to mast				________

- Places loads and removes loads from storage areas smoothly			________

- Takes precautions for entering trailers, and prevents exhaust exposure		________

- Excellent use of forklift controls							________

Other observations: ______________________________________________________________________________________________________________________________________________________________
_____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________