| LOCATION: | DATE: |
| --- | --- |
| TIME OF INSPECTION(S): | START OF SHIFT: |
| WEATHER CONDITIONS: | APPROX. TEMP.: |
| CHANGE IN WEATHER: | CHANGE IN CONDITIONS: |
| CREW LEADER: | SUPERVISOR: |
| DIMENTIONS: | DEPTH = |  | Yes No HAZARDOUS CONDITIONS |
|  | TOP = | W | L | Saturated soil / standing or seeping water |
|  | BOTTOM = | W | L | Cracked or fissured wall(s) |
| SOIL TYPE: | TESTED: | Bulging wall(s) |
| Solid rock (most stable) Class A | Yes | Floor heaving |
| Average soil Class B | No | Frozen soil |
| Fill material Class C | Super-imposed loads |
| Loose sand Class C | Vibration |
| Benching allowed in Class A and B soil Benching is not allowed in Class C Soil | Depth greater than 10’ |
|  | All Utilities Located |
| PROTECTION METHODS: | PLACEMENT OF SPOILS & EQUIPMENT |
| (Walls MUST be vertical—NO voids) | Spoils at least 2 feet from edge of trench |
| SHORING | Equipment at least 2 feet from edge |
| Timber | Backhoe at end of trench |
| Pneumatic | Compressor, etc. at remote location |
| Hydraulic | LADDER LOCATION |
| Screw Jacks | Located in protected area |
| Trench Shield | Within 25 feet of safe travel |
| UNEVEN, IRREGULAR WALLS | Secured |
| Trench Box | Extends 36 inches above the landing |
| Sloping: ( 1:1 (45°) ( 1 ½:1 (34°) | Leads to safe landing |
| Yes No ENVIRONMENTAL CONDITIONS: | OTHER: |
| Gas detector used? Required when trench is more than 4 feet deep | Shoring equip & materials inspected prior to use? |
| Confined space permit issued? | Is trench SAFE to enter? |
| COMMENTS: |
| NOTE | All unsafe conditions must be corrected prior to trench entry. If any hazardous conditions are observed, the trench must be immediately evacuated and no one is allowed to re-enter until corrective action has been taken. | TO BE FILLED OUT BY COMPETENT PERSON Excavation Entry Authorized By: Competent Person |

# Text boxes

Note: For trenches over 5 feet deep a protective system is required if the trench is not in stable rock. Trenches less than 5 feet deep may still require a protective system where kneeling or squatted work is performed unless determined unnecessary by a competent person based on the stability of the soil. Excavations over 20 feet deep require a registered professional engineer.